CHAPTER IV.

EFFECTS  OF GRAVITY

# Gravitational interaction of extended objects

- the formula for the gravitational interaction is valid for point-like objects

- what we do for extended objects ? (the

practically important cases)

- as a first approximation: apply the same formula for the center of masses!!!! ( the distance r used in , is the distance between the center of masses.

# Gravity near the Earth’s surface

-gravitational forces acting on a given object varies with the geographical location

-depends on height (for every 3 meter

height decreases by one part in a million)

( g varies with elevation

-for the same elevation g varies with

underground deposits

-due to the deformed sphere shape of the

Earth (ellipsoid) g varies with latitude

(smallest near the  Equator and increases

toward each pole)

Satellites and Planets

- Gravitation provides the centripetal force needed for the circular motion of the satellites and planets.

- Orbits in reality: ellipses  (circular orbits is a reasonable approximation)

- Main formulas governing satellite motion:

- Centripetal force = Gravitational force

(   ;

(m: the mass of the satellite,

M: mass of the Earth

V: speed of the satellite on the orbit

R: distance from the center of Earth)

- period of rotation (T)

(

(higher is the satellite’s orbit the longer it

takes to complete it.)

- influences of the gravitational forces exerted by other objects or planets can be taken into account applying the same formula for gravitational interaction (computations by a computer)

- movements of planets around the Sun obey the same rules.

## Tides

- ~ two high tides and two low tides each 24 hours (interval between successive high tides: 12 hours and 25 minutes)

- consequence of:

gravitational forces between water and Moon and

water and Earth

inertial forces from the rotation of the E-M system

around their center of mass and

rotation of the E around it’s axes.

rotation of the Earth around it’s axes

Inertial forces: -forces acting relative to

accelerating  systems

-does not obey the 3rd Law of  Newton

(have no reaction force)

-if  is the acceleration of the  system, the

inertial force acting on each body in the

system is

Bodies on a rotating system experience the:

centrifugal force (an inertial force)

How far Does Gravity Reach ?

infinite range !

- it accounts for the planets motion within the Solar system

- accounts for the structure and dynamics of the whole Universe: motion of stars, galaxies etc.

- Newton’s law of gravitation valid for each case

When mass and velocities are not too big…..

( the right description is by general relativity theory

- is G constant in time and the same everywhere???

# The concept of gravitational fields

Gravitation( sort of an action-at-a-distance interaction

- there is no direct pushing or pulling mechanism

- one mass modify the space surrounding it, the other mass is influenced by this modified space

concept of: gravitational field

- calculating the gravitational force in two steps:

I. determining the field from the first mass

II. calculating the force that this fields exerts

on the second mass

- the field concept will be very valuable tool !

- gravitational field vector: characterizing the gravitational field in each point around an object( it is the force experienced by a 1 kg probe mass at the given point

- Home-work assignments: 100/35-38;  100/40-43;

100/46-47 ; 100/53 ; 100/55; 101/10-17; 101/22

# Text boxes

Influence of Sun: Much smaller (although the gravitational attraction of Sun on Earth is 180 times bigger than of the Moon)

IMPORTANT:

The difference on the gravitational force on different parts of the Earth!